## Slide 1: Smart-Vents

## Slide 2: Benefits:
Automatically re-direct airflow to the rooms in your house that need it.
Increase comfort and save on energy bills
Control vents in hard to reach places

## Slide 3: How it works: The hardware
Prototyped 2 vents:
Vent1: + + +
Vent2: + + +
Arduino Nano
ESP8266-Wifi
28BYJ-48
DS18B20 sensor
Servo / Step Motor
HXT-900

## Slide 4: The hardware: what we learned
Servo is easier to implement for a DIY project
Step motor is more durable/quiet, would be better for a production unit
Using the ESP8266 wifi module was difficult (steep learning curve)

## Slide 5: How it works: Big picture
Step 1: Vents send temperature in a php GET request to web server.
Step 2: Server responds with the vent position.
Step 3: Vent position is parsed and vent moves accordingly.

## Slide 6: How it works: Server flow-chart
Vent 1
Vent1.php
Vent1.txt
Dashboard.php
VentSettings.php
settingsArray.json
Thermostat.php
Vent1pos.txt
Vent2pos.txt
Vent2
Vent2.php
Vent2.txt

## Slide 7: Challenges:
ESP8266 module- steep learning curve (trial and error)
Constant updates- refreshing server with out loosing settings / data on page (used files to store data)
Learning to program the arduino (youtube tutorials)

## Slide 8: Not enough time:
More vent settings / options in dashboard
Direct communication between vents / local server
Use Ajax to streamline server process
Integration with home thermostat
Separate temp sensor from vent
Cordless / solar power